## Slide 1
IoT Subteam
Project Echo Induction
Everything you need to get started with our Raspberry Pi 3 + Python + MQTT stack.
Raspberry Pi 3
Python
MQTT
Mixed levels welcome

## Slide 2
What is covered
01
Team & Project Overview
02
Hardware
03
Dev Environment Setup
04
Team Workflows
05
Getting Started

## Slide 3
01 / Team & Project Overview
What is Project Echo
Project Echo is a bioacoustics tool aimed at aiding conservationists in their efforts to protect endangered species. Using AI-driven audio analysis, Project Echo classifies and tracks animal vocalizations in their natural habitats through a network of microphones, offering a non-invasive solution to monitor wildlife.
Where we fit
As a member of the Project Echo IoT team you’ll be responsible for the physical aspects of the project: sensing and capturing audio and environmental data in the field and reliably transmitting it to the various other teams.
Our primary tech stack
Raspberry Pi 3 · Python · MQTT (Paho) · TensorFlow Lite
Key contacts
Team Lead - your primary point of contact
Subteam Members - listed in the team channel
Project Lead - for cross-team matters
Project Mentor - for additional concerns

## Slide 4
02 / Hardware
Development Board
Project Echo currently runs on a Raspberry Pi 3. While this gives us more processing and communication headroom, please keep resource usage low. The goal is to eventually deploy on a cheaper, lower-powered board, so design with that constraint in mind. A handy interactive pinout diagram of the Raspberry Pi 3 can be found at pinout.xyz
Sensors
GPS/GLONASS (U-blox7)
Mini USB microphone
Unknown brand, similar to this.
Planned additional sensors are a temperature/humidity sensor (likely DHT22) and an ambient light sensor (BH1750)
As of T1 2026 Project Echo consists of 2 sensors with plans to add an additional 2 sensors in the near future
USB GPS module: Datasheet
Power Management
The T1 2026 team is developing a dedicated power management solution incorporating a solar panel and battery bank, intended for future deployment. In the meantime, the project is powered by an Innowa 2-in-1 wireless charging set, a temporary measure that won't scale to the project's long-term needs.

## Slide 5
03 / Dev Environment Setup
Below are the requirements for working on the Project Echo IoT code.
1
Clone the repo
git clone https://github.com/DataBytes-Organisation/Project-Echo.git
2
Copy project requirements file
Located in Project-Echo/src/Components/IoT/edge_inference copy the requirements.txt file to wherever you want to create your virtual environment.
3
Create virtual environment
python -m venv (your environment name)
source (your environment name)/bin/activate
pip install -r server_requirements.txt

## Slide 6
04 / Team Workflows
Git Branching
main - stable, tested code only
For your tasks create a branch with the following convention: EIOT/[your initials]/[task name]
At the end of each sprint submit a PR; team lead reviews before merging
Task Management
Your team lead will assign your task(s) at the beginning of each sprint
Tasks are tracked in team project board
Update with task progress weekly in the MS teams channel
Raise roadblocks with team lead early, don't sit on them
Meetings & Communications
Weekly meeting with IoT team
Weekly meeting with Project Mentor
All meetings are planned in their respective MS teams group chats with additional communications, please ensure you are checking and answering these groups often.
File structure
Our current team code and work can be found at Project-Echo/src/Components/IoT
Research, previous implementations and prototypes can be found at Project-Echo/src/Prototypes/IoT
Keep PRs small and focused

## Slide 7
05 / Getting Started
These are the first steps you should take as part of your capstone journey with the Project Echo IoT team.
1
Join company/project OnTrack
2
Attend first company wide meeting
3
Introduce yourself in the IoT team chat
4
Setup dev environment
5
Investigate project files (IoT and prototype)
6
Attend first IoT team meeting
7
Receive onboarding task in IoT teams channel
8
Submit first PR
Stuck? Feel free to ask in the IoT team channel, or the Project Echo channel. There are no dumb questions.

## Slide 8
You're ready to build!
Welcome to the IoT subteam.
Repo & codebase — ask team lead for access
Team channel — ask for invite link
Broker credentials — ask team lead
Hardware inventory — ask team lead